## Slide 1
HKMC Gen2 mcu std
Renesas solution Vs competitors

## Slide 2: HKMC 2nd Standard MCU Pool list
Group | Renesas | IFX | NXP | STM | OthersGr
Gr. B | U5L2/4 (Candidate) | CYT2Bx | S32K31x (S32K312, S32K314) |  | 
Gr. C (ASIL-B) | U5L6/8 (Candidate) | CYT3BBx/4Bxx CYT4BFx | S32K32x (Candidate) (S32K322, S32K324, S32K328) | SPC58ECx | 
Gr. C (ASIL-D) | U2A6 | TC36x |  | SPC58NHx | 
Gr. D | U2A8/16 | TC38x | S32K38x (Candidate) (S32K388, S32K389) | SR6P3,SR6P3E (Candidate) | 

## Slide 3
Arm®
Renesas Core
Super Low Power
Power Efficiency
High Performance
32-bit MCU
32/64-bit SOC/MPU
16-bit MCU
Scalable with SOC
Renesas provides for the various needs of our customers with a rich lineup of automotive MCUs and MPUs.
Lighting
Motor
Control
AD
Gateway
IVI
ADAS
Power
Train
Chassis
Zone
Motor
Control
Tiny
Footprint
Super Low
Power
Broadest
Portfolio
Motor
Control
BCM
Chassis
Zone
Power Efficiency
FuSa
Hypervisor
Broadest
Portfolio
Power Efficiency
FuSa
Cyber
Security
Many
Cores
Large
Internal RAM
Linux
RTOS
Sensor
Switch
New
Renesas Automotive MCU and SOC/MPU
New Arm®-based MCU enhances RENESAS’ automotive portfolio to foster scalability to its SOCs

## Slide 4: Renesas MCU roadmap
12 MRAM
22 MRAM
28nm
28nm
40nm
Under Planning
Under Development
U2A
RH850 (2+2)->(4+4) 400MHz
16M
6M
ICU-MH
1Gbps / 100Mbps
U2C
RH850 (1+1)->(2+2) 320MHz
8M
2M
ICU-MH
1Gbps / 100Mbps / 10BT1S
U2B
RH850 (2+2)->(6+4) 400MHz
24M
6M
ICU-MH
1Gbps / 100Mbps / 10BT1S
U5H
R52 (X+Y) M55 (X+Y)
XXXMHz -> YYYMHz
32M MRAM
8M MRAM
RSIP
2.5Gbps / 1Gbps / 10BT1S
HYP
DSP
RTG ACC
U5M
M55 (1+1)->(4+2)
240MHz -> 400MHz
16M MRAM
2M
RSIP
1Gbps / 100Mbps / 10BT1S
RTG ACC
U5L
M33 (1+0)-> M55 (2/3+0)
160MHz -> 320MHz
8M MRAM
1M
RSIP
1Gbps /100Mbps / 10BT1S
C5x
R52 (16+0) 1.2GHz
M33 RT 400MHz
32M+ MRAM
16M MRAM
RSIP
2.5Gbps / 1Gbps / 10BT1S
AI ACC
HYP
RTG ACC
Mass Production
Under Consideration
F1
RH850 (1+0)->(2+0)
120-240MHz
8M
1M
ICU-S/M
100Mbps
P1
RH850 (1+1)->(2+2)
120-240MHz
8M
512K
ICU-S/M
100Mbps
C1
RH850 (1+1)->(2+1)
240-320MHz
4M
2M
ICU-S/M
E2
RH850 (2+2)->(6+4)
400MHz
16M
8M
ICU-M
100Mbps
HYP
HYP
10Base T1S
Notes: This is the RH850 U2Ax series roadmap. We’ve also added the RH850 F1x and P1x devices to the graphic. On the left, we’ve positioned the Chassis applications toward the bottom and the Body applications toward the top. It’s clear from the positioning that the P1x series covers Chassis and F1x covers Body. On the right side, we’ve added the U2Ax devices. The “x” in U2Ax designates the Flash size in megabytes. We have committed to offering 3 flash-size options of U2Ax: 16, 8, 6MB, and we are considering a lower-memory option of 3MB. Also note that the roadmap designates the level of Security. The F1x and P1x devices have limited security ICU-S (intelligent cryptographic unit- slave) or ICU-M (intelligent cryptographic unit- master), but they do not support the Evita-full standard. U2Ax devices, however, all support Evita-fill standard with ICU-MH units, which stands for intelligent cryptographic unit master – High performance).
Greg Bac…
Good slides, summarize the portfolio nicely.
One minor point, the E2M is a 40nm part while the E2Gx, E2UH, E2H are 28nm parts….. so a split nodes in one family….. Makes it a challenge for the MCAL software and explaining to customers.

## Slide 5: MCU Product positioning
CoGW(Low)
Zone Control
Domain Control
Legacy Control
Ultra High Performance
With AP capability
Service Application support
Fast boot
Routing with latest comm IF
Standby, low power
Standard ASIL D function
Standby, low power
R-Car
C5x
Standard ASIL B function
Standby, low power
R-Car
U5L
R-Car
U5M
U2C
U2A
+ Routing
+ latest security
+ latest Comm. IF
+ low power
CAN XL/T1S
ISO21434
F1x
+ latest security
+ latest Comm. IF
R-Car S4
Integration capability with FFI
High Performance
SoC/MCU Requirements
R-Car
U5H
U2B-E
U2B

## Slide 6: HKMC standard mcu gen2
Range | Group |  | DMIPS | Program Flash | FuSa | Security (HSM) | OTA | Ta(℃) | No of Pin | Renesas Device | Infineon | NXP | STM | Comments
Mid Range | B |  | ~500 | 1MB ~ 4MB | ASIL-B | Evita Medium | A/B Swap, Dual Bank, RWW | 105℃ ↑ 125℃ ↑ | 48 ~ 2xx | U5L2/4 (candidate) | CYT2BLx, CYT2B9x | S32K312,314 |  | 
 | C |  | 600~1600 | 4MB ~ 8MB | ASIL-B ASIL-D | Evita Full | A/B Swap, Dual Bank, RWW | 105℃ ↑ 125℃ ↑ | 100 ~ 3xx | U5L6/8 (candidate) U2A6 | CYT4BFx, CYT3BBx, CYT4BBx, TC364D | S32K324, 328 (candidate) | SPC58ECx SPC58NHx | 
 | D |  | 1300~3200 | 4MB ~ 10MB | ASIL-D | Evita Full | A/B Swap, Dual Bank, RWW | 105℃ ↑ 125℃ ↑ | 144 ~ 5xx | U2A8/16 | TC387Q | S32K388(8MB), 389 (12MB) (candidate) | SR6P3 SR6P3E (Candidate) | 

## Slide 7: U5L2 competitiveness
    New Technology
      U5L2/4 based on latest 28nm Flash Technology
    Competitive CPU
      U5L2/4 based on ARM cortex-M33 core @240MHz
    New and wide range of peripherals
      Ethernet 10Base-T1S (OA3p)
      CAN XL
      SENT, I3C,
    ISO21434 and Evita-Full supported
    Latest Autosar version (R23-11) supported
Function | R-Car U5L2 | Traveo 2 CYT2B9 | S32K148 | S32K312 | S32K322
CPU | (1+0) x Cortex-M33 @ 240 MHz | (1+0) x Cortex-M4 @ 160 MHz | (1+0) x Cortex-M4F @ 112 MHz | (1+0) x Cortex-M7 @ 120 MHz | (2+0) x Cortex-M7 @ 160 MHz
Code Flash / Data Flash | 2 MB / 128 KB | 2 MB / 128 KB | 2 MB / 64KB | 2 MB / 128 KB | 2 MB / 128 KB
Total RAM | 288 KB | 256 KB | 256 KB | 192KB (incl. 96KB TCM) | 256KB (incl. 192KB TCM)
Security | EVITA-Full | eSHE & HSM Evita full | CSEc | HSE-B (EVITA-Full) | HSE-B (EVITA-Full)
Analog Interfaces | up to 58 ch | up to 67 ch | up to 64 ch | up to 48 ch | up to 48 ch
Ext. Memory Interfaces | SFMA | - | QuadSPI | - | QuadSPI
Digital Interfaces | CAN / CAN-FD, CAN-XL, LIN / UART,CXPI, SENT,SPI, I3C / I2C, I2S, Ethernet T1S, General I/O Port | CAN / CAN-FD, LIN / UART, CXPI, SPI, I2C General I/O Port | CAN/CAN-FD, LIN/UART, I2C, SENT, I2S, SPI, Flex IO emulation (UART, I2C, SPI, I2S), Ethernet AVB (10/100 Mbps), General I/O ports | CAN/CAN-FD, I2C, SPI, LIN/UART Flex IO emulation (UART, I2C, SPI, I2S, SENT, PWM), General I/O Port | CAN/CAN-FD, I2C, SPI, LIN/UART, I2S, Flex IO emulation (UART, I2C, SPI, I2S, SENT, PWM), Ethernet 100M AVB/TSN, General I/O Port
Functional Safety | ASIL-B | ASIL-B | ASIL-B | ASIL-B | ASIL-B
Power Supply | 3.0 to 5.5V Single Power Supply | 2.7 to 5.5V | 2.7 to 5.5V | 3.0 to 5 V | 3.0 to 5 V
Thermal | Ta = -40 to + 125°C | Ta = -40 to + 125°C | Ta = -40 to + 125°C | Ta = -40 to + 125°C | Ta = -40 to + 125°C
No Wait OTA | Yes | Yes | Yes | Yes | Yes

## Slide 8: U5L4 competitiveness
Function | R-Car U5L4 | Traveo2 CYT2BL | Traveo2 CYT3BB | Traveo2 CYT4BB | S32K314 | S32K324
CPU | (1+0) x Cortex-M33 @ 240 MHz | (1+0) x Cortex-M4 @ 160 MHz | (1+0)x Cortex-M7 @ 250 MHz | (2+0)x Cortex-M7 @ 250 MHz | (1+0)x Cortex-M7 @ 160 MHz | (2+0)x Cortex-M7 @ 160 MHz
Code Flash / Data Flash | 4 MB / 256 KB | 4MB / 128 KB | 4MB / 256 KB | 4MB / 256 KB | 4MB/ 128 KB | 4MB/ 128 KB
Total RAM | 864 KB | 512 KB | 768KB (incl. 16KB TCM) | 768KB (incl. 16KB TCM) | 512 KB (incl. 96KB TCM) | 512 KB (incl. 192KB TCM)
Security | EVITA-Full | eSHE & HSM Evita full | eSHE & HSM Evita full | eSHE & HSM Evita full | HSE-B (EVITA-Full) | HSE-B (EVITA-Full)
Analog Interfaces | up to 70 ch | up to 67 ch | up to 75 ch | up to 75 ch | up to 72 ch | up to 72 ch
Ext. Memory Interfaces | SFMA, MMCA | - | eMMC, SMIF(QSPI/HS-SPI) | eMMC, SMIF(QSPI/HS-SPI) | QuadSPI | QuadSPI
Digital Interfaces | CAN/CAN-FD, CAN-XL, LIN / UART,CXPI, SENT,SPI, I3C / I2C, I2S,General I/O Port, Ethernet T1S, Ethernet 100M | CAN/CAN-FD, LIN/ UART, CXPI, SPI, I2C, General I/O Port | LIN/UART, I2S, CAN/CAN-FD, I2C, SPI, 10/100 Ethernet | LIN/UART, I2S, CAN/CAN-FD, I2C, SPI, 10/100 Ethernet | CAN/CAN-FD, I2C, LIN/UART, I2S , Flex IO emulation (UART, I2C, SPI, I2S, SENT, PWM), Ethernet 100M TSN, General I/O Port, SPI | CAN/CAN-FD, I2C, LIN/UART, I2S, SPI, Flex IO emulation (UART, I2C, SPI, I2S, SENT, PWM), Ethernet 100M TSN, General I/O Port
Functional Safety | ASIL-B | ASIL-B | ASIL B | ASIL B | ASIL-B | ASIL-B
Power Supply | 3.0 to 5.5V Single Power Supply | 2.7 to 5.5V | 2.7 to 5.5V | 2.7 to 5.5V | 3.0 to 5 V | 3.0 to 5 V
Thermal | Ta = -40 to + 125°C | Ta = -40 to + 125°C | Ta = -40 to + 125°C | Ta = -40 to + 125°C | Ta = -40 to + 125°C | Ta = -40 to + 125°C
No Wait OTA | Yes | Yes | Yes | Yes | Yes | Yes
    New Technology
      U5L2/4 based on latest 28nm Flash Technology
    Competitive CPU
      U5L2/4 based on ARM cortex-M33 core @240MHz
    New and wide range of peripherals
      Ethernet 10Base-T1S (OA3p)
      CAN XL
      SENT, I3C,
    High Flash and RAM ratio (big internal RAM size)
      4MB : 864KB (4.6 : 1)
    ISO21434 and Evita-Full supported
    Latest Autosar version (R23-11) supported

## Slide 9: U5L6/8 competitiveness
Function | R-Car U5L8 (U5L6) | Traveo2 CYT4BF | S32K328 | S32K338
CPU | (3+0) x Cortex-M55 @ 320 MHz ((2+0) x Cortex-M55 @ 240 MHz) | (2+0) x Cortex-M7 @ 350 MHz | (2+0) x Cortex-M7 @ 240 MHz | (3+0) x Cortex-M7 @ 240 MHz
Code Flash / Data Flash | 8 MB / 384 KB (6 MB / 320 KB) | 8 MB / 256 KB (incl. 16KB TCM) | 8 MB / 128 KB | 8 MB / 128 KB
Total RAM | 1.5 MB (1MB) | 1 MB | 1 MB (incl. 192KB TCM) | 1 MB (incl. 384KB TCM)
Security | EVITA-Full (ISO21434) | eSHE, HSM Evita full | HSB-E | HSB-E
Analog Interfaces | up to 88 ch | up to 99 ch | up to 72 ch | up to 72 ch
Ext. Memory Interfaces | SFMA, xSPI | eMMC, SMIF(QSPI/HS-SPI) | QSPI | QSPI
Digital Interfaces | CAN / CAN-FD, CAN-XL, LIN / UART,CXPI, SENT,SPI, I3C / I2C, I2S,General I/O Port, Ethernet T1S, Ethernet 1G (Ethernet 100M) | CAN / CAN-FD, I2C, I2S, LIN / UART, General I/O Port, FlexRay, Ethernet AVB, SPI, 10/100/1000Mbit Ethernet up to 2ch | CAN/CAN-FD, I2C, I2S, LIN/UART, Flex IO emulation (UART, I2C, SPI, I2S, SENT, PWM), Ethernet TSN 1000M, General I/O Port, SPI | CAN/CAN-FD, I2C, LIN/UART, I2S, Flex IO emulation (UART, I2C, SPI, I2S, SENT, PWM), Ethernet TSN 1000M, General I/O Port, SPI
Functional Safety | ASIL-B | ASIL-B | ASIL B | ASIL B
Power Supply | 3.0 to 5.5V Single Power Supply | 2.7 V to 5.5 V | 3.0 to 5 V | 3.0 to 5 V
Thermal | Ta = -40 to + 125°C | Ta = -40 to + 125C | Ta = -40 to + 125°C | Ta = -40 to + 125°C
No Wait OTA | Yes | Yes | Yes | Yes
    New Technology
      U5L6/8 based on new 22nm Technology
      No 6MB product in competitor roadmap
    Competitive CPU
      U5L6/8 based on ARM cortex-M55 core
    New and wide range of peripherals
      Ethernet 10Base-T1S (OA3p)
      CAN XL
      SENT, I3C
    High Flash and RAM ratio (big internal RAM size)
      8MB : 1.5MB (5.3 : 1)
    ISO21434 and Evita-Full supported
    Latest Autosar version (R23-11) supported

## Slide 10: U2A6 competitiveness
Function |  |  | RH850/U2A6 | TC364DP
CPU |  |  | G4MH | TC1.6.2
Speed | PE Core + Lockstep |  | 400MHz (2+2) | 300Mhz (2+2)
Operating Voltage (Core, #1, #2 selectable) |  |  | 2.7-5.5V | 1.25V, 3.3V, 5V
Flash | ROM | Size | 6MB | 4MB
 | DATA Flash | Size | 256KB | 256KB
RAM(Local + Retention) |  |  | 768KB | 672KB
Function | Timer | Timer | GTM, TAUD, TAUJ, TAPA, TSG3, ENCA, OSTM, WDTB, TPBA, RTC, PWM-Diag, TPTM, LTSC | STM, GTM, GPT12, CCU6
 | ADC | DS ADC | - | 4
 | Others | Others | 39~79 | 70
 | Communication | CAN-FD | 7~12 | 8
 | I2C | Flexlay | 2 | 1
 | UART | Ethernet | 0~1(100Mb) | 1(1Gb)
 |  | 10base-T1S | - | -
 | SPI | LIN | 8-12 | 12
 | - | SENT | 6~8 | 10
 | GPIO |  | 77~165 | -
Operating temperatures |  |  | –40 to +160 °C (Tj) | –40 to +125 °C
Package |  |  | 144Pin(HLQFP) 156Pin(FLBGA) 176pin(HQFP) 292Pin(FBGA) | 144pin(T/LQFP) 176pin(LQFP) 292pin(LFBGA) 180pin(BGA)
Safety |  |  | ASIL-D | ASIL-D
Security |  |  | EVITA-FULL | EVITA-FULL
    New Technology
      28nm Flash Technology
    Memory Scalability
      6MB, 8MB & 16MB variation Vs 4MB & 10MB
    High CPU performance
      400MHz G4MH core
      Max. 3KDMIPS Vs 1.4KDMIPS Max.
    Bigger internal RAM size
      768MB
    Autosar version (R22-11) supported

## Slide 11: U2A8/16 competitiveness
Function |  |  | RH850/U2A16 | RH850/U2A8 | TC387QP | S32K388 | S32K389
CPU |  |  | G4MH | G4MH | TC1.6.2 | Cortex M7 | Cortex M7
Speed | PE Core + Lockstep |  | 400MHz 4+4) | 400MHz (2+2) | 300Mhz(4+2) | 320MHz (4+1 or 3+2) | 300MHz (4+1 or 3+2)
Operating Voltage (Core, #1, #2 selectable) |  |  | 2.7-5.5V | 2.7-5.5V | 1.25V, 3.3V, 5V | (5V, 3.3V, or 5V & 3.3V split I/O domains) | (5V, 3.3V, or 5V & 3.3V split I/O domains)
Flash | ROM | Size | 16MB | 8MB | 10MB | 8MB | 12MB
 | DATA Flash | Size | 320KB | 320KB | 640KB | 128KB | 256KB
RAM(Local + Retention) |  |  | 3584KB | 1792KB | 1568KB | 1152KB | 2.3MB
Function | Timer | Timer | GTM, TAUD, TAUJ, TAPA, TSG3, ENCA, OSTM, WDTB, TPBA, RTC, PWM-Diag, TPTM, LTSC | GTM, TAUD, TAUJ, TAPA, TSG3, ENCA, OSTM, WDTB, TPBA, RTC, PWM-Diag, TPTM, LTSC | STM,GTM,GPT12,CCU6 | BCTU, LCU, 3x 4ch 24bit eMIOS, 3x LPCMP | BCTU, LCU, 3x 4ch 24bit eMIOS, 3x LPCMP
 | ADC | DS ADC | - | - | 10 | - | -
 | Others | Others | 79~94 | 79~94 | 124 | 3x 24ch 12 bit ADC | 3x 24ch 12 bit ADC
 | Communication | CAN-FD | 16 | 16 | 12 | 8 | 12
 | I2C | Flexlay | 4 | 4 | 2 | - | -
 | UART | Ethernet | 1/1(100Mb/1Gb) | 1/1(100Mb/1Gb) | 1(1Gb) | 2x 1Gbps Ethernet (TSN) | 2x 1Gbps Ethernet (TSN)
 |  | 10base-T1S | - | - | - | - | -
 | SPI | LIN | 12-24 | 12-24 | 24 | 16 | 16
 | - | SENT | 8 | 8 | 25 | 32x FlexIO (UART,I2C, SPI,I2S, SENT, PWM) + 6x SPI + 2x I2C + 2x I2S | 32x FlexIO (UART,I2C, SPI,I2S, SENT, PWM) + 6x SPI + 2x I2C + 2x I2S
 | GPIO |  | 165~301 | 165~211 | - | 235 | 330
Operating temperatures |  |  | –40 to +160 °C (Tj) | –40 to +160 °C (Tj) | –40 to +150 °C | –40 to +125 °C | –40 to +125 °C
Package |  |  | 292pin(FBGA) 373pin(FBGA) 516pin(FBGA) | 292pin(FBGA) 373pin(FBGA) | 516Pin(LFBGA) 292Pin(LFBGA) | 289pin(MAPBGA) | 437pin(MAPBGA)
Safety |  |  | ASIL-D | ASIL-D | ASIL-D | ASIL-D | ASIL-D
Security |  |  | EVITA-FULL | EVITA-FULL | EVITA-FULL | EVITA-FULL | EVITA-FULL
    New Technology
      28nm Flash Technology
      6MB, 8MB & 16MB variation Vs 4MB & 10MB
    High CPU performance
      400MHz G4MH core
      Max. 6KDMIP Vs Max. 4KDMIPS
    High Flash and RAM ratio (big internal RAM size)
      8MB : 1792KB (4.46 : 1)
      16MB : 3584KB ( 4.46 : 1 )
    Autosar version (R22-11) supported

## Slide 12
Renesas.com